EOCR-SSD

■ MCU( Microprocessor Control Unit ) Based/2-CT Type ■ Real Time Processing/Higher Preceision ■ Current Setting Range 05Type:0.5~6A/30Type:3~30A/60Type:10~60A ■ Indicating real current on the display ■ Trip cause digital display for easy trouble shooting ■ Reset:Manual(instantaneous)/Electrical(remote) ■ Load selection by DIP switch:Single phase(1P)/Three phase(3P) ■ Fail-safe(N)/Non-Fail-safe(R)

Protective Item Trip Time Descrption Over-current O-TIME Is<In Phase Loss 3 sec . Locked Rotor 0.5sec after elapse of dt >2times OC setting value

Over-Current Setting Current 05 0.5 ~ 6A 30 3.0 ~ 30A 60 10 ~ 60A Starting delay time D-TIME 1 ~30 sec Trip time O-TIME 0.5, 1~10 sec Operating t-c characteristic Over-Current Definite Tolerance Current ±5% TIME ±5% Environment Temperature Operation -20 ~60℃ Store -30 ~80℃ Humidity 30~85% RH Non-condensing Control Power 220 : 220VAC±15%, 50/60Hz 110 : 110VAC ±15%, 50/60Hz Output relay 2-SPST 3A / 250VAC Resistive Insulation Between casing and circuit Over 10MΩ, 500VDC Dielectric Strenghth Between casing and circuit 2000VAC 60Hz, 1min Between open contacts 1000VAC 60Hz, 1min between circuit 2000VAC 60Hz, 1min Reset Manual/Electrical Installation 35mm DIN-Rail or Panel Munting